## Slide 1: 第2部 RTコンポーネント作成入門
宮本 信彦
国立研究開発法人産業技術総合研究所
インダストリアルCPS研究センター
ソフトウェアプラットフォーム研究チーム

## Slide 2: 資料(USBメモリで配布)
2
ppt
  第2部
WEBページ(手順を記載したページ)
  第2部(Windows)
  第2部(Ubuntu)
installer
  OpenRTM-aistのインストールに問題があった場合に使用してください
script
  この講習で使うシミュレータのインストールスクリプト(Ubuntu用)
EXE
  RaspberryPiMouseSimulatorComp.exe(シミュレータ)
sample
  RobotController(本実習で作成するコンポーネントの見本)
Notes: 2

## Slide 3: インストールの確認(Windows)
3
OpenRTM-aist
  OpenRTM-aist-1.2.0-RELEASE_x86_64.msi
  Visual Studio 2019をインストールした場合はOpenRTM-aist-1.2.1-RC190514をインストールする
  インストール後に再起動する(2回再起動を必要とする環境もある)
Python
  python-2.7.16.amd64.msi
  OpenRTM-aistの64bit版をインストールする場合はPythonも64bit版をインストールする。
CMake
  cmake-3.14.1-win64-x64.msi
Doxygen
  doxygen-1.8.14-setup.exe
Visual Studio
  Visual Studio 2017 Community Edition
  もしくはVisual Studio 2019
  vs_installer_2019\vs_community__2112361810.1542592799_2019.exe
Notes: 3

## Slide 4: インストールの確認(Ubuntu)
4
OpenRTM-aist
  $ wget https://raw.githubusercontent.com/OpenRTM/OpenRTM-aist/master/scripts/pkg_install_ubuntu.sh
  $ sudo sh pkg_install_ubuntu.sh
CMake
  $ sudo apt-get install cmake cmake-gui
Doxygen
  $ sudo apt-get install doxygen
Java
  $ sudo apt-get install openjdk-8-jdk
Code::Blocks(任意)
  $ sudo apt-get install codeblocks
RaspberryPiMouseSimulatorComp
  $ wget https://raw.githubusercontent.com/OpenRTM/RTM_Tutorial_RaspberryPiMouse/master/script/install_raspimouse_simulator.sh
  sudo sh install_raspimouse_simulator.sh
Notes: 4

## Slide 5: 実習内容
5
シミュレータ上の車輪型移動ロボット(Raspberry Piマウス)の操作を行うコンポーネントの作成
  GUIにより目標速度入力
  センサ値が一定以上の場合に停止
Notes: 5

## Slide 6: Raspberry Piマウス概要
6
Raspberry Piマウスはアールティが販売している独立二輪駆動型の移動ロボット
Notes: 6

## Slide 7: 全体の手順
7
RTC Builderによるソースコード等のひな型の作成
ソースコードの編集、ビルド
  ビルドに必要な各種ファイルを生成
    CMakeにより各種ファイル生成
  ソースコードの編集
    RobotController.h、 RobotController.cppの編集
  ビルド
    Visual Studio、Code::Blocks
RTシステムエディタによるRTシステム作成、動作確認
  RTシステム作成
    データポート接続、コンフィギュレーションパラメータ設定
Notes: 7
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 8
コンポーネント開発ツール
RTC Builderについて

## Slide 9: RTC Builder
9
コンポーネントのプロファイル情報を入力し，ソースコード等のひな型を生成するツール
  C++、Python、Java、Luaのソースコードを出力
Notes: 9
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 10: RTC Builderの起動
10
起動する手順
  Windows(OpenRTM-aist 1.2)
    デスクトップのショートカットをダブルクリック
  デスクトップのショートカットがない場合
    Windows 7
      「スタート」→「すべてのプログラム」→「OpenRTM-aist 1.2.0」→「Tools」→「OpenRTP」
    Windows 8.1
      「スタート」→「アプリビュー(右下矢印)」→「OpenRTM-aist 1.2.0」→「OpenRTP」
      ※同じフォルダに「RTSystemEditorRCP」がありますが、これはRTC Builderが使えないので今回は「OpenRTP」を起動してください。
    Windows 10
      左下の「ここに入力して検索」にOpenRTPと入力して、表示されたOpenRTPを起動
  Ubuntu
    以下のコマンドを入力
    $ openrtp
Notes: 10
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 11: RTC Builderの起動
11
Windows 8.1
デスクトップ
スタート画面
アプリビュー
Notes: 11
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 12: RTC Builderの起動
12
Windows 10
左下の「ここに入力して検索」に「OpenRTP」と入力
Notes: 12
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 13: RTC Builderの起動
13
Notes: 13
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 14: RTC Builderの起動
14
Notes: 14
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 15: プロジェクト作成
15
RobotControllerコンポーネントのスケルトンコードを作成する。
  車輪型移動ロボット操作コンポーネント
    GUIでロボットを操作
    センサ値が一定以上の場合に停止
Notes: 15
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 16: 資料
16
USBメモリで配布
  「WEBページ」フォルダのHTMLファイルを開く
    チュートリアル(Raspberry Pi Mouse、C++、Windows、強化月間用) _ OpenRTM-aist.html
    チュートリアル(Raspberry Pi Mouse、C++、Windows、強化月間用) _ OpenRTM-aist.html
もしくはRTミドルウェア講習会のページからリンクをクリック
  チュートリアル(第2部、Windows)
  チュートリアル(第2部、Ubuntu)
Notes: 16
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 17: プロジェクト作成
17
Eclipse起動時にワークスペースに指定したディレクトリに「RobotController」というフォルダが作成される
  この時点では「RTC.xml」と「.project」のみが生成されている
以下の項目が設定する
  基本プロファイル
  アクティビティ・プロファイル
  データポート・プロファイル
  サービスポート・プロファイル
  コンフィギュレーション
  ドキュメント
  言語環境
  RTC.xml
Notes: 17
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 18: 基本プロファイルの入力
18
RTコンポーネントのプロファイル情報など，コンポーネントの基本情報を設定．
コード生成，インポート/エクスポート，パッケージング処理を実行
Notes: 18
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 19: 基本プロファイルの入力
19
モジュール名
  RobotController
モジュール概要
  任意(Robot Controller Component)
バージョン
  任意(1.0.0)
ベンダ名
  任意
モジュールカテゴリ
  任意(Controller)
コンポーネント型
  STATIC
アクティビティ型
  PERIODIC
コンポーネントの種類
  DataFlow
最大インスタンス数
  1
実行型
  PeriodicExecutionContext
実行周期
  1000.0
概要
  任意
Notes: 19
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 20: アクティビティの設定
指定アクティビティを有効にする手順
使用するアクティビティを設定する
Notes: 20
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 21: アクティビティの設定
21
コールバック関数 | 処理
onInitialize | 初期化処理
onActivated | アクティブ化されるとき1度だけ呼ばれる
onExecute | アクティブ状態時に周期的に呼ばれる
onDeactivated | 非アクティブ化されるとき1度だけ呼ばれる
onAborting | ERROR状態に入る前に1度だけ呼ばれる
onReset | resetされる時に1度だけ呼ばれる
onError | ERROR状態のときに周期的に呼ばれる
onFinalize | 終了時に1度だけ呼ばれる
onStateUpdate | onExecuteの後毎回呼ばれる
onRateChanged | ExecutionContextのrateが変更されたとき1度だけ呼ばれる
onStartup | ExecutionContextが実行を開始するとき1度だけ呼ばれる
onShutdown | ExecutionContextが実行を停止するとき1度だけ呼ばれる
Notes: 21
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 22: アクティビティの設定
22
以下のアクティビティを有効にする
  onInitialize
  onActivated
  onDeactivated
  onExecute
今回は練習のため、Documentationは空白でも大丈夫です
Notes: 22
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 23: データポートの設定
データポートを追加する手順
InPort、OutPortの追加、設定を行う
Notes: 23
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 24: データポートの設定
以下のOutPortを設定する
  out
    データ型： RTC::TimedVelocity2D
    他の項目は任意
    ※TimedVelocity3D型、TimedVector2Dと間違えないようにしてください
以下のInPortを設定する
  in
    データ型： RTC::TimedShortSeq
    他の項目は任意
    ※TimedShort型と間違えないようにしてください。
データ型はドロップダウンリストから選択する
Notes: 24
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 25: データポートについて
連続したデータを通信するためのポート
以下の例はデータフロー型がpush、サブスクリプション型がflush、インターフェース型がcorba_cdrの場合
Notes: 25
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 26: RTC::TimedVelocity2D型について
ExtendedDataTypes.idlで定義されている移動ロボットの速度を表現するためのデータ型
  vx: X軸方向の速度
  vy: Y軸方向の速度(車輪が横滑りしないと仮定すると0)
  va: Z軸周りの角速度
vxで直進速度、vaで回転速度を設定
Notes: 26
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 27: コンフィギュレーションの設定
コンフィギュレーションパラメータを追加する手順
コンフィギュレーションパラメータの追加、設定を行う
Notes: 27
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 28: コンフィギュレーションの設定
以下のコンフィギュレーションパラメータを設定する
  speed_x
    データ型：double
    デフォルト値： 0.0
    制約条件：-1.5<x<1.5
    Widget：slider
    Step: 0.01
    他の項目は任意
  speed_r
    データ型：double
    デフォルト値： 0.0
    制約条件：-2.0<x<2.0
    Widget：slider
    Step: 0.01
    他の項目は任意
GUI(スライダー)による移動ロボットの操作ができるようにする
Notes: 28
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 29: コンフィギュレーションパラメータの制約、Widgetの設定
制約条件：0<=x<=100
Widget：slider
Step：10
制約条件：0<=x<=100
Widget：spin
Step：10
Widget：text
RT System Editorでコンフィギュレーションパラメータを編集する際にGUIを表示する
Notes: 29
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 30: コンフィギュレーションパラメータの制約、Widgetの設定
制約条件：(0,1,2,3)
Widget：checkbox
制約条件：(0,1,2,3)
Widget：ordered_list
制約条件：(0,1,2,3)
Widget：radio
Notes: 30
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 31: コンフィギュレーションの設定
以下のコンフィギュレーションパラメータを追加
  stop_d
    データ型：int
    デフォルト値： 30
    他の項目は任意
センサ値がこの値以上の場合に停止
Notes: 31
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 32: Raspberry Piマウスの距離センサ
Raspberry Piマウス実機には距離センサが搭載されている
  計測した値は物体までの距離が近いほど大きな値となる
シミュレータでもこのデータに近い値を計算して出力している
Notes: 32
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 33: ドキュメントの設定
各種ドキュメント情報を設定
今回は適当に設定しておいてください。
  空白でも大丈夫です
Notes: 33
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 34: 言語の設定
実装する言語，動作環境に関する情報を設定
Notes: 34
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 35: スケルトンコードの生成
基本タブからコード生成ボタンを押すことでスケルトンコードが生成される
  Workspace\RobotController以下に生成
    ソースコード
      C++ソースファイル(.cpp)
      ヘッダーファイル(.h)
        このソースコードにロボットを操作する処理を記述する
    CMakeの設定ファイル(CMakeLists.txt)
    rtc.conf、RobotController.conf
    以下略
生成したファイルの確認
  作成したプロジェクトを右クリックして、「表示方法」→「システムエクスプローラー」を選択する
  エクスプローラーでワークスペースのフォルダが開くため、上記のファイルが存在するかを確認する
Notes: 35
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 36: 手順
36
ビルドに必要な各種ファイルを生成
  CMakeにより各種ファイル生成
ソースコードの編集
  RobotController.hの編集
  RobotController.cppの編集
ビルド
  Windows： Visual Studio
  Ubuntu： Code::Blocks
Notes: 36
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 37
ソースコードの編集、RTCのビルド

## Slide 38: CMake
38
ビルドに必要な各種ファイルを生成
  CMakeLists.txtに設定を記述
    RTC Builderでスケルトンコードを作成した時にCMakeLists.txtも生成されている
Notes: 38
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 39: ビルドに必要なファイルの生成
39
CMakeを使用する
  Windows 7
    「スタート」→「すべてのプログラム」→「CMake」→「CMake (cmake-gui)」
  Windows 8.1
    「スタート」→「アプリビュー(右下矢印)」→「CMake」→「CMake (cmake-gui)」
  Windows 10
    左下の「ここに入力して検索」にCMakeと入力して表示されたCMake(cmake-gui)を起動
  Ubuntu
    コマンドで「cmake-gui」を入力
Notes: 39
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 40: cmake-guiの起動
40
Windows 8.1
デスクトップ
スタート画面
アプリビュー
Notes: 40
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 41
41
Windows 10
cmake-guiの起動
左下の「ここに入力して検索」に「cmake」と入力
Notes: 41
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 42: ビルドに必要なファイルの生成
42
CMakeLists.txtをcmake-guiにドラックアンドドロップ
  CMakeLists.txtはRTC Builderで生成したプロジェクトのフォルダ
  (例： C:\workspace\RobotController)
Notes: 42
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 43: ビルドに必要なファイルの生成
43
Notes: 43
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 44: ビルドに必要なファイルの生成
44
Notes: 44
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 45: CMake 3.14以降の場合
45
ビルド環境の設定
Visual Studio 2017 → Visual Studio 15 2017
Visual Studio 2013 → Visual Studio 12 2013
※貸し出したPCでは「Visual Studio 14 2015」を指定
X64を選択する。
設定後、Finishボタンを押す
Notes: 45
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 46: CMake 3.13以前の場合
46
Notes: 46
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 47: ビルドに必要なファイルの生成
47
Notes: 47
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 48: ビルドに必要なファイルの生成
48
Notes: 48
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 49: ソースコードの編集
49
Notes: 49
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 50: ソースコードの編集
50
CMake-guiのバージョンが古い場合は「Open Project」ボタンがないため、ファイルをダブルクリックして開く
  Windows
    buildフォルダの「RobotController.sln」をダブルクリックして開く
  Ubuntu
    buildフォルダの「RobotController.cbp」をダブルクリックして開く
Notes: 50
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 51: ソースコードの編集
51
Windows
  Visual Studioが起動
Ubuntu
  Code::Blocksが起動
Notes: 51
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 52: ソースコードの編集
52
RobotController.hの編集
Visual Studio
Code::Blocks
Notes: 52
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 53: ソースコードの編集
53
RobotController.hの編集
Notes: 53
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 54: ソースコードの編集
54
RobotController.cppの編集
  詳細はUSBメモリの資料を参考にしてください
Visual Studio
Code::Blocks
Notes: 54
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 55: ソースコードの編集
55
RobotController.cppの編集
Notes: 55
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 56: ソースコードの編集
56
RobotController.cppの編集
Notes: 56
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 57: ソースコードの編集
57
データを読み込む手順
Notes: 57
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 58: ソースコードの編集
58
データを書き込む手順
Notes: 58
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 59: ソースコードのコンパイル
59
Visual Studio
Code::Blocks
  成功した場合、実行ファイルが生成される
    Windows
      build\srcフォルダのRelease(もしくはDebug)フォルダ内にRobotControllerComp.exeが生成される
    Ubuntu
      build/srcフォルダにRobotControllerCompが生成される
Notes: 59
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 60
システム構築支援ツール
RT System Editorについて

## Slide 61: RT System Editor
61
RTCをGUIで操作するためのツール
  データポート、サービスポートの接続
  アクティブ化、非アクティブ化、リセット、終了
  コンフィギュレーションパラメータの操作
  実行コンテキストの操作
    実行周期変更
    実行コンテキストの関連付け
  複合化
  マネージャからRTCを起動
  作成したRTシステムの保存、復元
Notes: 61
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 62: RT System Editorの起動
62
Notes: 62
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 63: RT System Editorの画面構成
63
Notes: 63
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 64: RobotControllerコンポーネントの動作確認
64
シミュレータコンポーネントと接続してシミュレータ上のロボットを操作するRTシステムを作成する
  ネームサーバーを起動する
  RaspberryPiMouseSimulatorコンポーネントを起動する
    Windows
      配布USBメモリのEXEフォルダ内「 RaspberryPiMouseSimulatorComp.exe 」をダブルクリック
    Ubuntu
      配布USBメモリ内のスクリプトでインストール(インストールしていない場合)
        $ sh install_raspimouse_simulator_usb.sh
      RasPiMouseSimulatorRTCに移動して以下のコマンドを実行
        $ build/src/RaspberryPiMouseSimulatorComp
  RobotControllerコンポーネント起動
  RaspberryPiMouseSimulatorコンポーネントとRobotControllerコンポーネントを接続して「All Activate」を行う
Notes: 64
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 65: ネームサーバーの起動
65
オブジェクトを名前で管理するサービス
  RTCを一意の名前で登録する
    RT System Editor等のツールはネームサーバーから名前でRTCの参照を取得する
起動する手順
Notes: 65
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 66: ネームサーバーの起動
66
OpenRTM-aist 1.1.2以前の手順
  Windows 7
    「スタート」→「すべてのプログラム」→「OpenRTM-aist 1.2.0」→「Tools」→「Start Naming Service」
  Windows 8.1
    「スタート」→「アプリビュー(右下矢印)」→「OpenRTM-aist 1.2.0」→「Start Naming Service」
  Windows 10
    左下の「ここに入力して検索」にStart Naming Serviceと入力して起動
  Ubuntu
    $ rtm-naming
Notes: 66
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 67: RobotControllerコンポーネントの動作確認
67
シミュレータコンポーネントと接続してシミュレータ上のロボットを操作するRTシステムを作成する
  ネームサーバーを起動する
  RaspberryPiMouseSimulatorコンポーネントを起動する
    Windows
      配布USBメモリのEXEフォルダ内「 RaspberryPiMouseSimulatorComp.exe 」をダブルクリック
    Ubuntu
      配布USBメモリ内のスクリプトでインストール(インストールしていない場合)
        $sudo sh install_raspimouse_simulator_usb.sh
      RasPiMouseSimulatorRTCに移動して以下のコマンドを実行
        build/src/RaspberryPiMouseSimulatorComp
  RobotControllerコンポーネント起動
    Windows
      build\srcフォルダのRelease(もしくはDebug)フォルダ内にRobotControllerComp.exeが生成されているためこれを起動する
    Ubuntu
      build/srcフォルダにRobotControllerCompが生成されているためこれを起動する
  RobotControllerコンポーネント、RasPiMouseSimulatorコンポーネントを接続して「All Activate」を行う
Notes: 67
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 68: データポートの接続
Notes: 68
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 69: データポートの接続
Notes: 69
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 70: データポートの接続
Notes: 70
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 71: アクティブ化
Notes: 71
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 72: コンフィギュレーションパラメータの操作
72
コンフィギュレーションパラメータをRT System Editorから操作する
以下の動作ができるか確認
  シミュレータ上のロボットがスライダーで操作できるか？
  ロボットが障害物に近づくと停止するか？
Notes: 72
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 73: 動作確認
73
タッチセンサがオンになった時に停止した場合
タッチセンサがオンになっても停止しない場合
壁まで前進する
壁の手前に停止する
壁に接触後も前進を続ける
Notes: 73
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 74: RTコンポーネントの状態遷移
RTCには以下の状態が存在する
  Created
    生成状態
    実行コンテキストを生成し、start()が呼ばれて実行コンテキストのスレッドが実行中(Runnning)状態になる
    自動的にInactive状態に遷移する
  Inactive
    非活性状態
    activate_componentメソッドを呼び出すと活性状態に遷移する
    RT System Editor上での表示は青
  Active
    活性状態
    onExecuteコールバックが実行コンテキストにより実行される
    リターンコードがRTC_OK以外の場合はエラー状態に遷移する
    RT System Editor上での表示は緑
  Error
    エラー状態
    onErrorコールバックが実行コンテキストにより実行される
    reset_componentメソッドを呼び出すと非活性状態に遷移する
    RT System Editor上での表示は赤
  終了状態
Notes: 74
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 75: RTコンポーネントの状態遷移(生成直後)
Notes: 75
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 76: RTコンポーネントの状態遷移(アクティブ化)
Notes: 76
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 77: システムの保存
Notes: 77
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 78: システムの復元
以下の内容を復元
  ポート間の接続
  コンフィギュレーション
  「Open and Create Restore」を選択した場合はマネージャからコンポーネント起動
Notes: 78
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 79: 非アクティブ化、終了
非アクティブ化
終了
Notes: 79
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 80: RTコンポーネントの状態遷移(非アクティブ化)
Notes: 80
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 81: Raspberry Piマウス実機との接続
Raspberry PiとノートPCを無線LANで接続
  Raspberry Piが無線LANアクセスポイントになる
注意事項
  ノートPCに複数のネットワークインターフェースが存在する場合にRTCの通信ができなくなる可能性があります。
    問題が発生した場合は個別に対応します。
  Raspberry Piアクセスポイント接続後はインターネットに接続できなくなります。
  Raspberry Piアクセスポイント接続後に、起動済みのネームサーバーとRTCは再起動してください。
  Raspberry Piはシャットダウンしてから電源スイッチをオフにするようにしてください
  モーター電源スイッチはこまめに切るようにしてください
Notes: 81
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 82: Raspberry Piとの接続
Raspberry Piの電源投入
  内側のスイッチをオンにする
電源を切る場合
  3つ並んだスイッチの中央のボタンを1秒以上押す
  10秒ほどでシャットダウンするため、その後に電源スイッチをオフにする
Notes: 82
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 83: Raspberry Piとの接続
無線LANアクセスポイントとの接続
  SSID、パスワードはRaspberry Piマウス上のシールに記載
  接続手順(Windows)
    画面右下のネットワークアイコンをクリック
    raspberrypi_xxに接続後、パスワードを入力
Notes: 83
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 84: ネームサーバーとの接続
Notes: 84
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 85: 起動済みのRTC、ネームサーバー再起動
ネームサーバーを再起動する
  OpenRTM-aist 1.2の場合はネームサーバー起動ボタンで再起動
  OpenRTM-aist 1.1.2の場合はネームサーバーのプロセス終了後、「Start Naming Service」を再度実行
RTC再起動
  RTCをexitするか、RTC起動時に表示したウインドウの×ボタンを押して終了する
  実行ファイル(RobotControllerComp.exe)を再度実行
Notes: 85
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 86: ポートの接続
RobotController0とRapberryPiMouseRTC0を接続する
Notes: 86
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 87: 動作確認
モーターの電源投入
  外側のスイッチをONにする
RTCをアクティブ化して動作確認
Notes: 87
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 88: リセット
RTCがエラー状態に遷移した場合にエディタ上には赤く表示される。
以下の操作で非アクティブ状態に戻す
Notes: 88
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 89: RTコンポーネントの状態遷移(エラー)
Notes: 89
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 90: RTコンポーネントの状態遷移(リセット)
Notes: 90
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 91
RTC Builder
補足

## Slide 92: サービスポートの設定
サービスポートの追加、インターフェースの追加、設定を行う
Notes: 92
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 93: サービスポートの設定
インターフェースを追加する
Notes: 93
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 94: サービスポートの設定
コード生成後、Pythonの場合はidlcompile.bat(idlcompile.sh)を起動する
インターフェースの設定を行う
Notes: 94
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 95: サービスポートの設定
IDLファイルについて
  プログラミング言語に非依存のインターフェース定義言語
コンシュマー側でプロバイダ側のecho、get_valueなどのオペレーションを呼び出す
Notes: 95
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 96: RTC Builderに関する設定
Notes: 96
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 97: RTC Builderに関する設定
Notes: 97
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 98: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
  IDLファイルを作成する
    MyDataType.idlを任意のフォルダ(ここではC:\UserDefType)作成
    別のIDLファイルをインクルードしている場合は同じフォルダにコピーする
Notes: 98
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 99: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
  RTC Builderの設定でIDLファイルの存在するディレクトリを追加
Notes: 99
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 100: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
Notes: 100
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 101
RT System Editor
補足

## Slide 102: コネクタプロファイルの設定
項目 | 設定内容
Name | 接続の名称
DataType | ポート間で送受信するデータの型．ex)TimedOctet,TimedShortなど
InterfaceType | データを送信方法．ex)corba_cdrなど
DataFlowType | データの送信手順．ex)push, pullなど
SubscriptionType | データ送信タイミング．送信方法がPushの場合有効．New, Periodic, Flushから選択
Push Rate | データ送信周期(単位：Hz)．SubscriptionTypeがPeriodicの場合のみ有効
Push Policy | データ送信ポリシー．SubscriptionTypeがNew，Periodicの場合のみ有効． all，fifo，skip，newから選択
Skip Count | 送信データスキップ数．Push PolicyがSkipの場合のみ有効
Notes: 102
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 103: コネクタプロファイルの設定
InterfaceTye
  データの送信方法
  1.1.2ではcorba_cdr(CORBAによる通信)のみ選択可能
  1.2.0では以下の通信方法も選択可能になる予定
    direct(同一プロセスで起動したRTC間でデータを直接変数に渡す)
    shared_memory(共有メモリによる通信)
DataFlowType
  データの送信手順
    Push
      OutPortがInPortにデータを送る
    Pull
      InPortがOutPortに問い合わせてデータを受け取る
SubscriptionType
  データ送信タイミング(DataFlowTypeがPush型のみ有効)
    flush(同期)
      バッファを介さず即座に同期的に送信
    new(非同期)
      バッファ内に新規データが格納されたタイミングで送信
    periodic(非同期)
      一定周期で定期的にデータを送信
Push Policy(SubscriptionTypeがnew、periodicのみ有効)
  データ送信ポリシー
    all
      バッファ内のデータを一括送信
    fifo
      バッファ内のデータをFIFOで１個ずつ送信
    skip
      バッファ内のデータを間引いて送信
    new
      バッファ内のデータの最新値を送信(古い値は捨てられる)
Notes: 103
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 104: コネクタプロファイルの設定
DataFlowType
  Push
  Pull
Notes: 104
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 105: コネクタプロファイルの設定
SubscriptionType
  flush(同期)
  new、 periodic(非同期)
Notes: 105
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 106: コネクタプロファイルの設定
項目 | 設定内容
Buffer length | バッファの大きさ
Buffer full policy | データ書き込み時に，バッファフルだった場合の処理．overwrite，do_nothing，blockから選択
Buffer write timeout | データ書き込み時に，タイムアウトイベントを発生させるまでの時間(単位:秒)
Buffer empty policy | データ読み出し時に，バッファが空だった場合の処理．readback，do_nothing，blockから選択
Buffer read timeout | データ読み出し時に，タイムアウトイベントを発生させるまでの時間(単位:秒)
Notes: 106
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 107: サービスポートについて
コマンドレベルのやり取りを行うための仕組み
  任意のタイミングで操作を行いたい時などに使用
    例えばロボットアームのサーボを停止させる、ハンドを閉じる等
コンシューマ側がプロバイダ側が提供する関数群(オペレーション、メソッド)を呼び出す
インターフェースはIDLファイルで定義する。
Notes: 107
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 108: サービスポートの接続
Notes: 108
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 109: コンフィギュレーションパラメータについて
パラメータを外部から操作する仕組み
  コンポーネント作成後に変更が必要なパラメータを設定する
    例えばデバイスが接続されているCOMポート番号の設定等
Notes: 109
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 110: コンフィギュレーションパラメータの設定
Notes: 110
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 111: コンフィギュレーションパラメータの設定
方法1
方法2
Notes: 111
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 112: マネージャの操作
CameraViewerComp.exe、OpenCVCameraComp.exeのプロセスではマネージャが起動している
  マネージャがコンポーネントを起動する
Notes: 112
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 113: マネージャの操作
Notes: 113
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 114: マネージャの操作
マスターマネージャの起動、RT System Editorからの操作によるRTCの生成までの手順を説明する
  rtc.confの設定
    「manager.is_master」を「YES」に設定して起動するマネージャをマスターに設定する
      manager.is_master: YES
    モジュール探索パスの設定
      manager.modules.load_path: ., C:\\Program Files (x86)\\OpenRTM-aist\\1.1.2\\Components\\C++\\Examples\\vc12
  作成したrtc.confを設定ファイルの指定してrtcd.exeを起動する
    rtcdはコマンドプロンプトからrtcd.exeを入力するか、OpenRTM-aistをインストールしたフォルダからコピーして使用する
    rtcdはマネージャの起動のみを行う
      ～Comp.exeは起動時に特定のコンポーネントの起動も行う
    RT Syetem Editorのネームサービスビューにマネージャが表示される
Notes: 114
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 115: マネージャの操作
モジュールのロード
Notes: 115
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 116: マネージャの操作
モジュールのロード
Notes: 116
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 117: マネージャの操作
RTCの生成
Notes: 117
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 118: 実行コンテキストの操作
Notes: 118
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 119: 実行コンテキストの操作
実行周期の設定
Notes: 119
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 120: 実行コンテキストの操作
実行コンテキストの関連付け
  RTC起動時に生成した実行コンテキスト以外の実行コンテキストと関連付け
    関連付けた実行コンテキストでRTCを駆動させる
  他のRTCとの実行を同期させる
Notes: 120
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 121: 実行コンテキストの操作
実行コンテキストの関連付け
Notes: 121
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 122: 複合コンポーネントの操作
複合コンポーネントの生成
Notes: 122
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 123: 複合コンポーネントの操作
複合コンポーネントの生成
Type
  以下の3種類から選択可能
    PeriodicECShared
      実行コンテキストの共有
    PeriodicStateShared
      実行コンテキスト、状態の共有
    Grouping
      グループ化のみ
Notes: 123
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 124: 複合コンポーネントの操作
Notes: 124
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 125: 複合コンポーネントの操作
Notes: 125
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 126: ゾンビの削除
RTCのプロセスが異常終了する等してネームサーバーにゾンビが残った場合、以下の手順で削除する
Notes: 126
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 127: RT System Editorに関する設定
Notes: 127
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.